## Slide 1
CARBON FOOT PRINT
Training 4
Development of green energy competences for energy stability
ID KA220-HED-E683AE00
Authors:
Dejan Blagojevic, Aleksandra Boričić, Boban Cvetanovic- AATPS,
Filip Kokalj, Niko Samec UNI Maribor,
Mitko Kostov, Gordana Janevska, Stojanče Nusev, UKLO
Ljiljana Kostić Despotović JugoImpex,
Angelina Petrevska- MZT

## Slide 2: What is a Carbon Footprint?
A carbon footprint is the total amount of greenhouse gases (GHGs) emitted directly and indirectly by an organization, activity, or individual, typically expressed in equivalent tons of carbon dioxide (CO2e).
Energy Consumption: Emissions resulting from the use of electricity, heating, and cooling systems.
Transportation: Emissions from vehicles used for commuting, transportation of goods, and travel.
Waste Production: Emissions associated with waste generation, disposal, and treatment processes.
Water Use: Emissions from the treatment and distribution of water.

## Slide 3: Measuring the Carbon Footprint of an Institution

## Slide 5: Define the Scope
Scope 1: Direct emissions from owned or controlled sources (e.g., on-campus heating).
Scope 2: Indirect emissions from the generation of purchased electricity, steam, heating, and cooling.
Scope 3: Other indirect emissions that occur in the value chain (e.g., employee commuting, waste disposal, and business travel).

## Slide 6: Data Collection:
Energy Use: Gather data on electricity and fuel consumption, including heating, cooling, and equipment usage.
Transportation: Collect information on vehicle miles traveled, fuel consumption, and modes of transportation used by employees and students.
Waste Management: Track the amount and type of waste produced, and the methods used for disposal and recycling.
Water Consumption: Measure the amount of water used and the energy required for treatment and distribution.

## Slide 7: Elements for calculation
1. Energy Consumption
2. Transportation
3. Waste Management
4. Water Use
5. Agriculture
6. Building Materials
7. Food Consumption

## Slide 8: 1. Energy Consumption
Electricity: The emission factor varies significantly by region and energy source. On average, in the U.S., the emission factor for electricity is approximately 0.4 kg CO2e per kWh. However, this can be lower in areas with high renewable energy penetration and higher in regions reliant on fossil fuels.
Natural Gas: About 0.185 kg CO2e per kWh generated.
Heating Oil: Approximately 2.52 kg CO2e per liter burned.
Coal: Roughly 2.3 kg CO2e per kWh generated.

## Slide 9: Transportation
Passenger Vehicles: Average emission factor for
  gasoline vehicles is about 0.192 kg CO2e per mile.
  disel vehicles is about 0.192 kg CO2e per mile.
  electric vehicles is about 0.192 kg CO2e per mile.
Light-Duty Trucks: Approximately 0.215 kg CO2e per mile.
Buses: About 0.075 kg CO2e per passenger mile (depending on occupancy).
Air Travel:
  Domestic flights emit about 0.254 kg CO2e per passenger mile;
  international flights can vary but are generally higher.

## Slide 10: Waste Management
Landfilling: About 0.6 kg CO2e per kg of waste sent to landfill.
Incineration: Around 0.9 kg CO2e per kg of waste.
Recycling: Emission reductions vary by material but are generally negative (i.e., they reduce emissions).

## Slide 11: Water Use
Water Treatment and Distribution:
Approximately 0.001 kg CO2e per liter of water treated and distributed.

## Slide 12: Agriculture
Enteric Fermentation (Livestock): Emission factors can vary widely, but for beef cattle, it is around 70 kg CO2e per kg of beef produced.
Manure Management: About 0.02 kg CO2e per kg of manure.
Fertilizer Application: Approximately 0.003 kg CO2e per kg of fertilizer applied.

## Slide 13: Building Materials
Cement: Roughly 0.8 kg CO2e per kg of cement produced.
01
Steel: Approximately 1.8 kg CO2e per kg of steel produced.
02
Wood: Can vary, but a rough estimate is 0.1 kg CO2e per kg of wood used (considering transportation and processing).
03

## Slide 14: Factors Influencing Carbon Footprint
Square Meters (m²) of Facility Space
The size of the building affects energy consumption, as larger spaces typically require more energy for heating, cooling, and lighting.
Emissions from the facility can be estimated based on the energy usage per square meter, which varies depending on the type of building and its energy efficiency.
Number of Employees
The number of employees can impact the carbon footprint through commuting, office supplies, and general resource consumption.
More employees typically lead to higher emissions from transportation and increased resource usage in the workplace (e.g., paper, electricity).

## Slide 15: GREENES CALCULATOR

## Slide 16: report

## Slide 17: Strategies for Reducing Carbon Footprint
Energy Efficiency:
Upgrade Infrastructure: Invest in energy-efficient lighting, HVAC systems, and appliances.
Conduct Energy Audits: Regularly assess energy use and implement recommendations to reduce consumption.
Renewable Energy:
Invest in Renewable Sources: Utilize solar panels, wind turbines, or geothermal systems to power the institution.
Purchase Green Energy: Buy renewable energy certificates (RECs) or engage in power purchase agreements (PPAs) with green energy suppliers.
Sustainable Transportation:
Promote Public Transport: Encourage the use of public transport, carpooling, or biking among students and staff.
Provide Incentives: Offer incentives for using electric vehicles, such as charging stations and subsidies.
Waste Reduction and Management:
Implement Recycling Programs: Establish comprehensive recycling and composting initiatives to reduce waste sent to landfills.
Reduce Single-Use Plastics: Encourage reusable containers and utensils on campus.
Water Conservation:
Install Water-Saving Fixtures: Use low-flow faucets, toilets, and irrigation systems to reduce water consumption.
Educate on Water Use: Raise awareness about water conservation practices among students and staff.
Carbon Offsetting:
Support Carbon Offset Projects: Invest in reforestation, renewable energy projects, or community-based initiatives that offset emissions.
Engagement and Education:
Raise Awareness: Conduct workshops and seminars on sustainability practices and their importance.
Involve the Community: Engage students, faculty, and staff in sustainability initiatives and encourage feedback on potential improvements.

## Slide 18
https://greenes.akademijanis.edu.rs/en