## Slide 1: Modern Hydro Power Plants
Prof. Dr.sc. Gordana Janevska

## Slide 2: Hydro Power Plants: Basics, types and classification, principle of operation
Energy utilization
Electricity generation and consumption
Types of power plants
Types of Hydropower Plants
  Types of hydroelectric power plants according to the method of water utilization
  Types of hydroelectric power plants based on the available head
  Types of hydroelectric power plants according to installed capacity
  Hybrid hydropower
Environmental and Social Aspects of Hydro Power Plants
  Fish migration
  Sedimentation
  Water quality
  Environmental flows
  Hydropeaking
  Mitigation hierarchy
Principle of Operation of Hydroelectric Power Plants
  Available and useful energy head of the turbine
  Turbine Power and Efficiency

## Slide 3: 1.1. Energy utilization
The second half of the 19th century - new method emerged for harnessing energy from fuels and water
The mechanical power derived from thermal energy is transformed into electrical energy, which is transmitted through power lines to the point of use, where it is converted back into mechanical work, heat, or some other form of energy.
The advantages of electrical energy - can be economically transmitted over long distances and easily converted into various forms of energy
‘Electricity production‘ - the process of generating electric energy for industrial and public electrification purposes. Energy is not produced but rather converted from one form to another, it is so widely used that it is also retain here.
The electric power industry, or energy industry, aims to convert different forms of energy into electrical energy and deliver it to end-users through the most cost-effective methods. Electric power industry is responsible for the production of electrical energy. This branch of the energy sector focuses on various energy conversions to provide economically efficient services.
The production and use of electrical energy are of paramount importance both in the economy and in people's everyday lives today. With the help of electrical energy, any place on the Planet can be connected to modern production processes and embrace the cultural aspects of contemporary living.
Hydro Power Plants:
Basics, types and classification, principle of operation

## Slide 4: 1.2. Electricity generation and consumption
Usable electricity is not freely available in nature, so it must be "produced" (that is, transforming other forms of energy to electricity). Production is carried out in power stations (also called "power plants"). Electricity is most often generated at a power plant by electromechanical generators, primarily driven by heat engines fueled by combustion or nuclear fission. There are also other energy sources such as the kinetic energy of flowing water and wind, as well as other alternative energy sources including solar photovoltaics and geothermal energy.
Phasing out coal-fired power stations and eventually gas-fired power stations, or, if practical, capturing their greenhouse gas emissions, is an important part of the energy transformation required to limit climate change. Vastly more solar power and wind power is forecast to be required, with electricity demand increasing strongly with further electrification of transport, homes and industry.
Electricity consumption represents the actual energy demand from the existing electricity supply, which is used for various purposes such as transportation, housing, industry, commerce and others.
Hydro Power Plants:
Basics, types and classification, principle of operation

## Slide 5: 1.2. Electricity generation and consumption
Hydro Power Plants:
Basics, types and classification, principle of operation
Share of the different sources in the total electricity generation (2019)
Consumption, production, net import of electricity in the Republic of North Macedonia
The global electricity consumption in 2019 amounted to 22,848 terawatt-hours (TWh), approximately 135% higher than the consumption level in 1990 (9,702 TWh). China, the United States, and India accounted for over 50% of the global share in electricity consumption.

## Slide 6: 1.2. Electricity generation and consumption
The share of hydropower in energy production varies significantly in the energy sector among different countries and depends on the available water potential. It should be emphasized that the development of energy sector in all countries is moving towards the complete utilization of all available water potentials, regardless of future energy sources. The reasons for this are as follows:
The driving 'fuel' is inexhaustible and constantly available, thanks to solar energy.
Hydropower plants, with rational use, help in solving water management problems related to river basins and their water flows, thereby benefiting the entire water system.
Furthermore, hydropower plants contribute to solving issues such as flood protection, erosion, river navigability, and groundwater protection.
Hydropower plants serve as an energy source that helps protect the environment, which will be a central concern globally in the coming decades.
Hydro Power Plants:
Basics, types and classification, principle of operation

## Slide 7: 1.3. Types of Power Plants
Electric power plants are facilities where various forms of energy are converted into electricity. They represent complex technical systems composed of different machines and devices that are interconnected. Each component in the power plant can be treated as a separate system, making the power plant a highly organized and complex system, i.e., the power plant can be characterized as a higher-order system.
One of the possible classifications of electric power plants is:
According to the type of energy they produce,
According to the fuel they use,
According to the area they supply with electricity.
Hydro Power Plants:
Basics, types and classification, principle of operation

## Slide 8: 1.3. Types of Power Plants
According to the type of energy they produce, they are divided into:
Direct current power plants, and
Alternating current power plants.
According to the fuel source, power plants are divided into:
Fossil fuel power plants,
Hydro power plants,
Wind power plants,
Solar power plants, and
Nuclear power plants.
According to the area they supply with electricity, power plants are classified as:
Industrial,
Marine (shipboard),
Urban,
Regional,
National.
Hydro Power Plants:
Basics, types and classification, principle of operation