## Slide 1: CONTEMPORARY PRODUCTION TECHNOLOGIES
Prof. dr. Stojanche Nusev

## Slide 2: Abrasive Jet Machining (AJM)
In this power point presentation there is detailed explanation of Abrasive Jet Machining (AJM), which evolves from traditional sandblasting techniques, used for cleaning castings and corroded surfaces. Unlike sandblasting, AJM uses fine abrasive particles propelled at high speeds to machine materials without physical contact.

## Slide 3: Abrasive Jet Machining (AJM)
Principles and Components:
Principle of Operation: The process involves abrasive particles, driven by gas pressure, passing through a nozzle to impact the material's surface. This method allows for precise material removal with minimal physical contact, thus reducing wear and tear on the tooling.
Equipment Setup: The AJM equipment consists of a nozzle, an abrasive feed system, and a gas drive system. The nozzles are typically made of hard metals like tungsten carbide and have very small openings to precisely direct the abrasive particles.
Material and Abrasives Used: Common abrasives include corundum and silicon powder, with alternatives like baking soda and glass for specific applications. The choice of gas fluid (air, CO2, N2) depends on the abrasive material used, with filters integrated to clean and dry the air when necessary.

## Slide 4: Abrasive Jet Machining (AJM)
Technological Features
Productivity Factors: Productivity in AJM depends on the type of abrasive, the material being machined, and the precise control of the jet's pressure and composition. The process allows for high accuracy and surface quality, especially on hard and fragile materials like ceramics and glass.
Applications: AJM is extensively used in industries requiring high precision and minimal material damage, such as electronics and medical instruments. It is also used for engraving and intricate cutting works in the glass industry.

## Slide 5: Abrasive Jet Machining (AJM)
Water Jet Processing
The document further discusses Water Jet Processing, which utilizes a high-pressure water stream, optionally mixed with abrasives, to achieve material processing.
Setup and Process
Equipment Configuration: The system consists of a pressure unit, abrasive hopper, and a nozzle system that can be controlled numerically for complex shape productions. The process often incorporates a robotic system for precise nozzle movement, especially when dealing with intricate or large-scale operations.
Material Compatibility: Water jet processing is noted for its versatility, capable of machining materials from soft tissues to hard metals without altering the material's inherent properties due to thermal effects.

## Slide 6: Abrasive Jet Machining (AJM)
Advantages and Applications
Advantages: The primary advantages include the absence of thermal distortion, high machining precision, and the ability to cut complex shapes without tool wear.
Industrial Use: It is particularly effective for materials that are difficult to process using conventional methods, with applications ranging from aerospace components to intricate artistic designs.

## Slide 7: Conclusion
Precision and Minimal Contact: Abrasive Jet Machining (AJM) and Water Jet Processing represent significant advancements in non-conventional machining, emphasizing precision and minimal physical contact with the material.
AJM Applications: AJM is particularly effective for delicate and hard materials, offering high accuracy without damaging the workpiece, making it ideal for use in precision-required industries like electronics and medical instruments.
Water Jet Versatility: Water Jet Processing excels in handling a diverse range of materials without thermal distortion, enabling intricate designs and applications across both industrial and artistic fields.
Adaptation to Advanced Materials: These technologies highlight the shift towards manufacturing processes that can accommodate advanced materials and complex designs, promoting innovation in product development.
Impact on Manufacturing Evolution: The integration of these advanced machining technologies is crucial for the ongoing evolution of manufacturing, enhancing capabilities and driving efficiency and sustainability in production processes.