## Slide 1: CONTEMPORARY PRODUCTION TECHNOLOGIES
Prof. dr. Stojanche Nusev

## Slide 2: Introduction to Chemical Processing
Historical Context: Prominent post-WWII, especially in aircraft industry.
Basic Principle: Controlled removal via chemical dissolution using acids or bases.
Protection Methods: Surfaces protected by masks or resistant coatings.
Techniques Used: Material immersed or sprayed depending on precision and part geometry.
Materials Applicable: Suitable for metals and alloys including aluminum, titanium, and steels.

## Slide 3: Chemical Processing Techniques
Surface Treatment Goals: To reduce weight without altering mechanical properties.
Etching and Engraving: Deeper removal for creating profiles or engravings.
Installation Types: Spraying or immersing in a chemical bath.
Process Stages: Involves roughing, fine finishing, and rinsing.
Equipment Example: Conveyor system for continuous processing.

## Slide 4: Chemical Agents and Masks
Caustic Agents: Various acids and bases, effectiveness depends on concentration and temperature.
Masking Techniques: Essential for protecting regions not subjected to etching.
Mask Types: Cut-scratched, photomasks, and printed masks for different precision needs.
Application Precision: Varies from ±0.05 mm for printed masks to ±150 µm for cut-scratched.
Industry Applications: Used in aerospace for weight reduction, pattern etching in electronics.
Etching parts by immersion in a bath

## Slide 5: Introduction to Electrochemical Processing
Fundamental Concept: Material removal through anodic dissolution using a current in electrolyte.
Historical Development: Known but used for machining only recently, reversing electroplating concept.
Faraday's Laws Application: Material dissolved proportional to the electric current.
Process Setup: Consists of cathode (tool), anode (workpiece), and electrolyte.
Electrochemical Reaction Example: Breaking down solutions into ions facilitating metal removal.

## Slide 6: Electrochemical Processing Techniques
Current Density Importance: Determines material removal rate, higher densities enable faster processing.
Tool Wear and Maintenance: Minimal wear provided electrolyte is non-corrosive.
Material Form After Removal: Forms metal hydroxides, separated by filtration methods.
Electrolyte Characteristics: Requires good thermal properties, minimal corrosiveness.
Installation Components: Includes power source, electrolyte circulation, and control systems.

## Slide 7: Advantages of Electrochemical Processing
Tool Longevity and Cost: Long lifespan and low cost due to minimal wear.
Surface Finish Quality: High-quality finishes with good manufacturing precision.
Operational Productivity: High throughput, beneficial for complex and hard-to-machine materials.
Cost Efficiency: Lower overall operational costs with cost-effective electrolytes.
Application Diversity: Used for various machining operations across multiple industries.

## Slide 8: Challenges and Limitations of Electrochemical Processing
Process Control: Requires maintaining precise working distances and controlled parameters.
Energy Consumption: Higher electricity use increasing operational costs.
Hydrogen Release: Management of hydrogen gas released during processing.
Tooling and Setup: Complex and potentially costly setup and maintenance.
Further Refinements Needed: Improvements essential for wider industrial adoption.

## Slide 9: Comparative Overview
Process Selection: Depends on material type, desired precision, and application requirements.
Material Compatibility: Chemical for various alloys, electrochemical for hard materials.
Precision and Complexity: Electrochemical offers higher precision for complex shapes.
Environmental Impact: Both require careful handling to minimize environmental impact.
Cost-Effectiveness: Each has economic advantages, suited for different applications.

## Slide 10: Future Trends in Material Processing
Technological Advancements: Enhancing precision, efficiency, and environmental safety.
Integration with Automation: Increasing use of automated systems for controlled processing.
Material Innovations: Adaptations in techniques to handle unique material properties.
Environmental Regulations: Influence of stricter controls on processing choices.
Global Industry Applications: Expanding use in emerging markets and sectors.

## Slide 11: Summary and Conclusion
Critical Role in Manufacturing: Vital roles in modern manufacturing, particularly in high precision sectors.
Selection Criteria: Influenced by material properties, complexity, environmental considerations, and costs.
Advancements and Improvements: Continued research and development to overcome limitations.
Industry Impact: Significant effects on aerospace, automotive, electronics, and medical industries.
Future Prospects: Expected growth in advanced manufacturing using these technologies.