## Slide 1: ENERGY EFFICIENCY OF CNC METAL CUTTING MACHINES COMPARED TO CONVENTIONAL MACHINES
Prof. dr. Stojanche Nusev

## Slide 2: INTRODUCTION
In order to reduce the environmental impact of the metal processing industry, it is essential to decrease electricity consumption during metal processing.
Reducing electricity and resource consumption during processing significantly impacts the entire life cycle of the resulting products.
In countries where electricity production relies heavily on fossil fuels, electricity consumption is a significant source of CO2 emissions. Consequently, higher electricity consumption during cutting processes increases the carbon footprint of product manufacturing.
Therefore various approaches are being explored to produce and process products using energy-efficient and environmentally friendly production methods on metal-cutting machines.

## Slide 3: METAL CUTTING MACHINES
Metal cutting machines, as their name suggests, are designed for processing metal objects. This process, known as machining, involves removing excess material from a metal workpiece, often resulting in a conical shape.
Due to rapid technological advancements, there are now various types of metal cutting machines categorized by their purpose, function, structural performance, and control method.
According to the control method, metal cutting machines can be categorized into two main groups:
  Conventional (manually operated) metal cutting machines,
  CNC (computer-controlled) metal cutting machines.

## Slide 4: METAL CUTTING MACHINES
In conventional metal cutting machines, the operator translates information from technological and technical documentation into control commands, which are manually activated on the machine. This process involves manually adjusting the machine’s working elements.
Manually operated metal cutting machines have limited productivity. To enhance productivity, manual machine functions are increasingly replaced with computer-controlled functions. As more tasks are automated, the role of manual control is shifted to computerized management.
With CNC (Computer Numerical Control) metal cutting machines, the operator’s role evolves from direct machine control to overseeing and managing the machine through a computer-based program. The operator's responsibilities shift from hands-on execution to organizing and controlling the machine's operations via the management software.

## Slide 5: DEFINITION OF ENERGY EFFICIENCY
In general linguistic terms, "efficiency" is defined as the ratio of output to input, reflecting the ability to perform an activity with minimal resource consumption.
According to the ISO 14955 standard for evaluating the environmental impact of metal cutting machines, energy efficiency is described as the ratio or other quantitative relationship between the output performance, services, products, or energy and the energy input. This definition aligns with Patterson's 1996 explanation of energy efficiency in the industrial sector, which characterizes it as the ratio of the useful output of a process to the energy input required for that process.

## Slide 6: ADVANTAGES OF CNC METAL CUTTING MACHINES OVER CONVENTIONAL MACHINES
The electrical energy consumed by metal cutting machines is a major factor influencing their energy efficiency during cutting processes.
Calculating, analyzing, assessing, and comparing electricity consumption between CNC (Fig. 1a) and conventional metal cutting machines (Fig. 1b) is a complex task. Various principles can be applied to evaluate and compare the energy efficiency of these two types of machines. These principles stem from the differences in operation between CNC and conventional machines in contemporary production processes.
Fig. 1: a) CNC, b) Conventional metal cutting machine

## Slide 7
The fact that both CNC and conventional metal cutting machines consume substantial amounts of electrical energy during production is unchanged. However, comparing the key advantages of CNC machines over conventional ones is crucial for assessing energy efficiency from various perspectives.
CNC metalworking machines are noted for their flexibility, high precision, and repeatability. They allow for the production of workpieces in both small and large batches by creating a single program, which can be easily modified or replaced to produce different workpieces.
When using CNC metal-cutting machines, the utilization efficiency of the machine increases. These machines allow for the simultaneous operation of multiple units due to reduced monitoring and control requirements, and they do not require highly skilled operators. The machine operator only needs to know how to set up, remove, measure the workpiece accurately, and use the appropriate program, which requires significantly fewer skills and less expertise compared to operating a conventional metal cutting machine.

## Slide 8
Increasing the number of coordinate axes in the working space of CNC metal-cutting machines (Fig. 2) simplifies the processing process compared to conventional metal-cutting machines (Fig. 3).
Figure 2: Workspace of Multi-Axis CNC Metal Cutting Machines
Figure 3: Operational Area of Conventional Metal Cutting Machines

## Slide 9
Production operations that would typically require various conventional metal cutting machines can be consolidated into a single operation on a suitable CNC metal cutting machine. This integration significantly reduces the number of operations, steps, and transitions, which is often not feasible with traditional metal cutting machines, both from a technical and economic perspective.
By minimizing the number of production operations, the need for production equipment is also reduced. This leads to fewer metal cutting machines, less workspace required for installation, and a decrease in the manpower and energy needed for operation and maintenance.
Overall, these factors highlight the enhanced energy efficiency of CNC metal cutting machines compared to their conventional counterparts. They achieve this through increased productivity, improved machine utilization time, a reduction in production operations, and simplified production processes.

## Slide 10: ENERGY EFFICIENCY IN CNC METAL CUTTING MACHINE UNITS
MAIN UNITS
The main units of a metal cutting machine are responsible for both the main and auxiliary movements within the machine.
The main movement is driven by the rotational motion of the main working spindle, which is powered by the main motion drive servo motor. Electrical energy supplied to this servo motor is converted into mechanical work through a suitable transmission mechanism, enabling the rotation of the main spindle and, consequently, the cutting of the workpiece.
Auxiliary movements are controlled by separate servo motors dedicated to each coordinate axis. These motors enable precise movement along each axis, ensuring accurate positioning and operation of the machine.

## Slide 11
Drive spindles are crucial components in metal cutting machines, as they power the working elements. Consequently, they play a significant role in determining the energy consumption of CNC machining processes.
Drive spindles are typically classified into three types: integrated motor spindles, indirectly driven spindles (which use a belt drive or gearbox between the motor and the spindle), and hybrid spindles (which combine elements of both). Integrated motor spindles are often preferred due to their high stiffness. Unlike indirectly driven spindles, they do not require gears or drive belts that would need additional cooling under high torque conditions. To minimize workpiece tolerance deviations, it is crucial to limit axial displacement caused by thermal effects.
When analyzing the indirectly driven spindle outside of machining conditions, it demonstrates a more favorable thermal performance. However, the overall efficiency of the spindle is diminished due to the limited mechanical efficiency of the gearbox. Most motor spindles use asynchronous electric motors, with synchronous electric motors being the second most common.
DRIVE SPINDLES (FOR MAIN MOVEMENT)

## Slide 12
The high demand for energy efficiency is driving the replacement of asynchronous electric motors with more energy-efficient synchronous motors. These more efficient motors generate less thermal dissipation, which in turn reduces the need for cooling and further lowers overall energy consumption. However, the push for greater power and spindle speed to enhance machine productivity can counteract the reduction of energy losses in the main spindles.
Figure 4: Efficiency diagram
Figure 4 displays a typical efficiency diagram for an asynchronous electric motor, highlighting the range where energy-efficient operation is most effective. By using synchronous electric motors, improved energy efficiency can be achieved at high loads and torques. However, energy efficiency significantly decreases at low torques and low speeds.
DRIVE SPINDLES (FOR MAIN MOVEMENT)

## Slide 13
Compared to drive spindles, which provide the primary motion, auxiliary motion drivers have relatively low electrical power requirements.
Despite this, these auxiliary drivers are crucial for energy efficiency due to their widespread use in automated metal cutting machines and their involvement in every machining process. By analyzing auxiliary movements, we can estimate how quickly a process can be completed and what requirements must be met to achieve it.
To enhance energy efficiency in production processes, auxiliary movements are simplified. Reducing the number of preparatory operations decreases the need for production, processing, and adjustment of special tools used for positioning work items and guiding cutting tools. This change significantly reduces preparation and finishing times in production processes.
For machines performing multiple combined production operations, minimizing both active and idle times can reduce the overall electrical energy consumption of the machines.
DRIVERS FOR AUXILIARY MOTION

## Slide 14
A double spindle system, for instance, can reduce electrical energy consumption by up to 80% compared to using two separate machines. Additionally, the reduced weight of these systems enhances structural performance and further decreases the electricity required for auxiliary movements.
It's important to note that CNC metal cutting machines, like their conventional counterparts, consume electricity not only during the cutting process but also while setting machine parameters, clamping tools, and measuring. This means that even when the cutting process is inactive and the machine is in “standby" mode, it still uses power.
To address this, some CNC metal cutting machines feature an automatic shutdown option, which puts the machine into "standby" mode. In this mode, the machine’s functions are deactivated, leading to electricity savings.
DRIVERS FOR AUXILIARY MOTION

## Slide 15
The support units in CNC metal cutting machines are implemented systematically. They are integrated into the control logic of the control unit and operate independently of the program management.
SUPPORT UNITS
COOLANT SYSTEM
Coolant systems primarily function to remove heat generated during manufacturing and processing, thereby maintaining the optimal temperature of various working components.
Additionally, cooling is crucial for the machine's control unit, which houses the steering and control electronics. Reliable operation of the coolant system is vital to ensure the machine's performance, as localized heat accumulation can lead to displacement of structural components and disrupt or permanently damage the machine's working elements.
In CNC metal cutting machines, the coolant system typically consumes the largest portion of energy. Enhancing the energy efficiency of the coolant system can be achieved through the optimization of individual components and the overall design of the system.

## Slide 16
COOLANT SUPPLY SYSTEM
The coolant supply system is essential for cooling and lubricating the working elements and for transporting chips from the cutting zone during the cutting process.
Using cutting fluids incurs substantial economic and environmental costs. Economically, these costs include procurement, processing, disposal of the cutting fluid, and the electricity required for pumps and associated equipment, such as filtration systems. Environmentally, cutting fluids can be harmful, posing health risks to machine operators and environmental damage if not disposed of properly.
Despite significant advancements in reducing coolant and lubrication use, these substances remain necessary for many production operations.
Figure 5: Stages of the cutting fluid circuit
Therefore, the cutting fluids supply system is typically designed as a closed-loop system with three phases: supply, transfer, and maintenance (Fig. 5). This design allows for optimized energy efficiency in each phase.

## Slide 17
LOW-PRESSURE CUTTING FLUID SUPPLY
The supply of coolant to the cutting zone can be achieved in two primary ways: through the use of nozzles or directly via the cutting tools. Specifically, jet channels with small openings are incorporated into the cutting tools to deliver coolant into the cutting zone.
Due to the constant flow resistance in these nozzle and tool channels, low-pressure pumps operating at a steady speed are employed to transfer the coolant. Properly sizing the pump is crucial for the effectiveness of the cooling system. Additionally, optimizing the design of the machine's cooling system and minimizing resistance in the nozzles and tools can further enhance energy efficiency.
However, even with the correct pump and a well-designed low-pressure cooling system, the potential for additional savings remains limited. This limitation arises because the coolant supply and other auxiliary systems, such as cutting fluid recirculation pumps, are activated by NC commands or switches, which are designed for need-based and energy-efficient operation.

## Slide 18
HIGH-PRESSURE CUTTING FLUID SUPPLY
Increasing the pressure and flow in pumps boosts their power. However, using an internal high-pressure cutting fluid feed enhances overall energy efficiency by significantly improving process stability and productivity.
High-pressure pumps for internal coolant supply typically operate at pressures between 80 and 100 bar, with some capable of reaching up to 300 bar. To ensure energy-efficient operation of these pumps in various metal cutting machines, it is essential to adjust the hydraulic power to accommodate different flow resistances.
For constant-speed pumps, this adjustment can be made using a bypass valve to relieve pressure under increased flow resistance. However, this method generally results in lower energy efficiency. Greater energy efficiency is achieved by managing the pump according to power supply needs through frequency converters.

## Slide 19
HIGH-PRESSURE CUTTING FLUID SUPPLY
The use of various cutting tools, each with distinct flow resistance values, affects the characteristics of the variable speed pump system. Therefore, optimizing pump performance based on the specific cutting tool in use can substantially enhance energy efficiency, as illustrated in Figure 6.
Figure 6: Pump characteristics and power demand for a machine tool with various cutting tools
Utilizing a pump with an internal high-pressure coolant supply can enhance the overall energy efficiency of the machine, provided the technology supports an increase in the material removal rate. This approach helps offset the temporarily higher energy consumption during processing, resulting in greater overall energy savings.

## Slide 20
HYDRAULIC SYSTEM
The hydraulic system facilitates various functions in metal cutting machines, such as tool changes, workpiece clamping, and weight compensation for vertical axes. It also supplies hydraulic pressure for hydrostatic bearings and guides.
Typically, the hydraulic system consumes up to 10% of the machine's total electricity. It also exhibits relatively high energy consumption during idle mode due to leakage losses.
To enhance the energy efficiency of the hydraulic system, several strategies are employed: using accumulators and pressure boosters, implementing variable-speed and variable-volume pumps, incorporating directional valves, and optimizing components to minimize leakage.
Reducing leakage through improved component design and the use of directional valves enhances energy efficiency. Energy savings potential increases with higher system pressure. However, the effectiveness of design improvements for pumps and accumulators can vary significantly depending on the machine’s configuration and the processes it performs.

## Slide 21
HYDRAULIC SYSTEM
Figure 7 illustrates the fundamental concepts for designing hydraulic systems in metal cutting machines. Variable-speed pumps paired with hydraulic accumulators offer an effective solution for situations requiring variable hydraulic power (see Fig. 7a). The accumulator allows for rapid response and the use of relatively small, low-power pumps. By utilizing multiple accumulators with a single pump, different pressure levels can be achieved. Additionally, the pump can be entirely deactivated when hydraulic power is not needed, minimizing leakage losses in the system.
As the thermal load on the hydraulic system increases due to frequent pump start-ups, this configuration becomes progressively less efficient.
Figure 7: Basic design concepts for hydraulic units in machine tools

## Slide 22
HYDRAULIC SYSTEM
Variable speed pumps, typically controlled by frequency converters, adjust the flow rate and system pressure according to demand (see Fig. 7b). These pumps offer an energy-efficient solution for machinery with varying hydraulic power needs. However, the absence of an accumulator can lead to higher pump power and continuous operation to address leakage.
Variable displacement pumps (see Fig. 7c) serve as an alternative to variable speed pumps for hydraulic power regulation, eliminating the need for frequency converters. They also require electricity to counteract leakage losses. In terms of energy efficiency, variable displacement pumps are effective for applications with high hydraulic power demands.
Given the complexity of metal cutting machines, adjusting hydraulic systems can be intricate, often involving multiple pumps and accumulators for both low and high-pressure cycles. Therefore, implementing individual measures or a combination of measures may result in interactions and potential synergies. Additionally, the composition of the hydraulic fluid can impact the system's energy efficiency.

## Slide 23
HYDRAULIC SYSTEM
There are several methods to reduce electricity consumption in hydraulic systems. For instance, implementing a directional valve and accumulators can cut electricity usage by up to 91%. Accumulators, in particular, are an energy-efficient choice for hydraulic systems that operate at low power levels.
Optimizing the hydraulic system can also be achieved by using two variable-volume pumps for low and high pressure. By employing a variable-speed pump for low pressure and a pressure booster, system leakage can be reduced by 79%. Additionally, using a high-pressure variable-speed pump, a pressure booster, and two separate accumulators for low and high pressure cycles can further optimize the system. In this setup, pressure losses during idle mode can be reduced by 90%, and the active power requirement is decreased by 26% compared to conventional hydraulic systems. This optimization minimizes thermal load and system losses, leading to significantly improved energy efficiency.

## Slide 24: ENERGY EFFICIENCY OF CNC METAL CUTTING MACHINES
Analyzing the energy efficiency of both the main and auxiliary systems to enhance their performance contributes significantly to the overall energy efficiency of CNC metal cutting machines.
Below, we present three different CNC metal cutting machines where improvements have been made to the energy efficiency of both the main and auxiliary systems. As a result, the overall energy efficiency of these machines has been substantially enhanced.

## Slide 25: ENERGY EFFICIENCY OF CNC METAL CUTTING MACHINES
In the first example (Fig. 8), an enhancement in the energy efficiency of a CNC metal-cutting machine, specifically the "Heller 2000," is demonstrated. This machine is used for milling and hole-making operations.
Figure 8: Exemplary saving potential for machining of a reference workpiece achieved in the research project EWOTeK
Enhancing the energy efficiency of individual systems boosts the overall efficiency of the machine used for producing the work item (as shown in the picture). Specifically, electricity consumption for the described processing has been reduced from 6.25 kWh to 4.38 kWh, representing a 30% decrease.

## Slide 26: ENERGY EFFICIENCY OF CNC METAL CUTTING MACHINES
In the second example (Fig. 9), the energy efficiency improvements of the CNC metal-cutting machine "MAG XS-211" are discussed. This machine is used for milling, fabrication, enlarging, and thread cutting of circular openings.
Figure 9: Exemplary saving potential for machining of a reference workpiece achieved in the research project Maxiem
Enhancing the energy efficiency of individual systems leads to an overall improvement in the energy efficiency of the machine used to produce the work object (as shown in the picture). Specifically, the electricity consumption for the processing has decreased from 0.78 kWh to 0.38 kWh, representing a 52% reduction.

## Slide 27: ENERGY EFFICIENCY OF CNC METAL CUTTING MACHINES
In the third example (see Fig. 10), an enhancement in the energy efficiency of the CNC metal-cutting machine "DMC 80 H duoBLOCK" is demonstrated. This machine is used for milling, both fine and rough, as well as for producing round holes.
Figure 10: Exemplary saving potential for machining of a reference workpiece achieved in the research project NCplus
Enhancing the energy efficiency of individual systems contributes to the overall efficiency of the workpiece processing machine (as illustrated in the figure). Specifically, the electricity consumption for this processing task was reduced from 22.3 kWh to 15.6 kWh, representing a 30% decrease.

## Slide 28: CONCLUSION
According to Patterson's definition of energy efficiency for metal cutting machines, the electrical energy used during the processing should be matched by the energy invested in the process.
Electricity consumption is determined by the processing time and the machine's electrical demand. Therefore, the total electricity demand of a metal cutting machine is used as a key input in calculating its energy efficiency.
Given that one CNC metal cutting machine can replace 3 to 8 conventional metal cutting machines, it can be concluded that CNC machines offer significantly better energy efficiency compared to their conventional counterparts.
The implementation of CNC metal cutting machines boosts productivity by up to 50%, enhances processing accuracy by 2 to 3 times, and reduces the number and cost of additional production operations by 4 to 8 times. However, the final energy efficiency of the machine is largely determined by the type of production operation performed.
By minimizing the electricity required to initiate and sustain cutting processes, these machines contribute to more energy-efficient manufacturing, which lowers the carbon footprint and conserves electricity.