## Slide 1: CONTEMPORARY PRODUCTION TECHNOLOGIES
Prof. dr. Stojanche Nusev

## Slide 2: NUMERICALLY CONTROLLED MACHINES
Computer Numerical Control is the process of manufacturing machined parts in a manufacturing environment controlled by a computerized controller that uses motors to move each axis. The controller actually controls the direction, speed and duration of movement of each motor. The programmed path is loaded into the machine's computer by the operator and then executed.
Numerical Control (NC) is the original term for this technology. It has been one of the main directions of development in production in the past fifty years, and it arose not only as a need to develop new techniques and achieve higher production levels, but also helped to increase the quality of products and to stabilize production costs
Introduction

## Slide 3: NUMERICALLY CONTROLLED MACHINES - NC DEVELOPMENT
A Historical Perspective:
Origins (1947): John Parsons initiated the use of numerically controlled machines with three-axis data manipulation for crafting aircraft parts.
Early Demonstrations (1912): Showcased a machine capable of simultaneous three-axis movement, setting a precedent for future developments.
Industrial Adoption (1911): Numerical control technologies were refined for industrial applications, enhancing manufacturing precision and efficiency.
Program Creation Techniques:
Initial Methods: Programs were manually inputted into machines similar to punching machines. Commands were entered line by line, and data was stored on perforated tapes read by NC machines.
Advancements in Storage Media:
Transitioned from perforated tapes to magnetic tapes to avoid physical damage and accommodate more data.
Magnetic diskettes became popular as a more durable and reusable medium, though they were still susceptible to environmental contaminants like dust and magnetic fields.

## Slide 4: NUMERICALLY CONTROLLED MACHINES - NC DEVELOPMENT
Modern Data Transmission:
From RS-232 to Modern Standards: The evolution from RS-232 serial ports to contemporary methods including USB, Internet, and wireless networks, marking significant progress in machine communication capabilities.
Significance:
This technological evolution underscores major strides in automation, paving the way for sophisticated manufacturing systems and increased production capacities across industries.

## Slide 5
NUMERICALLY CONTROLLED MACHINES - CNC MACHINES
Key Features:
Technological Advancements: CNC machines are equipped with built-in computers acting as controllers, offering more programmable functions than traditional NC machines.
Versatility: Can operate both as standalone units or interconnected within networks like flexible machining centers.
Ease of Programming: Supports multiple programming methods including keyboards, magnetic tape readers, diskettes, and electronic connectors for remote programming.
Core Objectives of Numerical Control:
Efficiency Boost: Aimed to increase production and reduce labor costs significantly.
Economic Production: Focus on cost-effectiveness and the ability to manufacture precision parts that were previously impossible or impractical.
Quality and Consistency: Enhances the accuracy and uniformity of parts, improving overall production quality.

## Slide 6
NUMERICALLY CONTROLLED MACHINES - CNC MACHINES
Advantages:
Productivity and Cost Efficiency: Increases output while reducing storage and preparation costs.
Operational Flexibility: Facilitates rapid design changes and improves control over production processes.
Quality Improvements: Achieves higher consistency in part manufacturing, backed by advanced production control mechanisms.
Challenges:
Increased Maintenance Costs: Higher expenses on electrical maintenance due to sophisticated technology.
Capital Investment: Requires significant upfront investment in machinery.
Operational Costs: Potentially higher per-hour costs compared to older machine tools.
Staff Training: Necessitates retraining for staff to handle advanced CNC operations.
Conclusion:
The development of CNC technology underscores a significant shift towards automation in manufacturing, aiming to address both the quantitative and qualitative demands of modern production environments.

## Slide 7: NUMERICALLY CONTROLLED MACHINES - BASIC COMPONENTS OF NUMA MACHINES
Core Components:
Processor Program: Houses essential commands for part processing, detailing the geometric data that outlines the trajectory of machine tools and their interaction with the workpiece.
Steering Unit: Acts as a microcomputer, loading and decoding the processing program to manage machine operations accurately.
Machine Structure: Executes the physical processing tasks as dictated by the program.

## Slide 8: NUMERICALLY CONTROLLED MACHINES - BASIC COMPONENTS OF NUMA MACHINES
Operational Details:
Programming Content: Includes crucial information such as cutting speeds, tool positions, and cooling agents which dictate the operational parameters.
Conversion Mechanism: Utilizes a regulated electric motor, typically DC, that drives a threaded spindle converting rotational movements into linear motions.
Advanced Positioning and Sensor Technology:
Position Measurement: Utilizes a position sensor linked with the spindle to measure and relay the position of the work table, ensuring precision in part placement.
Feedback System: Incorporates a comparator and digital-analog converter to adjust motor operations based on desired vs. actual position, enhancing accuracy and reducing errors.
Sensor Dynamics: Features an innovative sensor system where a rotating disc with perforations modulates light to a photodetector, translating rotational movements into digital signals for precise control.

## Slide 9: NUMERICALLY CONTROLLED MACHINES - BASIC COMPONENTS OF NUMA MACHINES
Engineering Innovations:
Light Sensitivity: NUMA's unique design minimizes external light interference, crucial in precision machining.
Threaded Spindle Design: Uses specialized threaded spindles with rolling nuts to reduce friction and wear, improving machine longevity and performance.
Conclusion:
These intricate systems and components underscore NUMA’s advanced capabilities in automating and refining manufacturing processes, allowing for high-precision production across various industrial applications.