## Slide 1: CONTEMPORARY PRODUCTION TECHNOLOGIES
Prof. dr. Stojanche Nusev

## Slide 2: UNDERSTANDING COORDINATE SYSTEMS AND MOVEMENTS IN NUMA
Fundamentals of Coordinate Systems:
Purpose: To unequivocally define machine movements within the working space, ensuring precision in manufacturing tasks.
Standardization: Each type of machine, such as lathes, milling machines, and drills, employs a universally recognized coordinate system embedded within the machine’s control unit software.
Axis Configuration:
Lathes: Typically operate on a two-axis system.
Milling Machines: Utilize a three-axis system to accommodate more complex operations.
Extended Capabilities: Advanced machining centers may operate on up to five axes, enhancing their ability to perform sophisticated manufacturing processes.

## Slide 3: UNDERSTANDING COORDINATE SYSTEMS AND MOVEMENTS IN NUMA
Axis Orientation:
Z-Axis: Always aligned parallel to the main spindle’s axis, directing movement from the workpiece towards the tool.
X and Y Axes: Dictate lateral and vertical movements respectively, with their positive directions standardized based on machine type.
Complex Axis Systems:
Additional Axes: In more complex machinery, additional axes (marked as u, c, and nj) parallel to the primary x, y axes are introduced to handle additional movement and rotation around the primary axes.

## Slide 4: UNDERSTANDING COORDINATE SYSTEMS AND MOVEMENTS IN NUMA
Coordinate Setting Methods:
Absolute vs. Relative Systems:
  Absolute System: Coordinates are set relative to a fixed origin point, ensuring consistency and simplicity in programming.
  Relative System: Each new movement takes the last position as the reference point, allowing dynamic adjustments during operations which is crucial for tasks requiring incremental changes.
Practical Implications: The choice between absolute and relative systems affects the programming approach, with absolute offering straightforward, uniform coordinates and relative providing flexibility by adapting to the machine’s current position.
Modern Control Units:
Dual System Compatibility: Most contemporary control units are versatile, supporting both absolute and relative coordinate settings, which significantly simplifies programming and enhances operational flexibility.
Programming Advantages: This dual capability allows programmers to select the most effective coordinate setting method based on specific operational requirements and machine capabilities.

## Slide 5: Types of Numerical Control in NUMA Systems
Core Management Styles of Device Movement:
Point-to-Point Management: Simplistic control where the machine moves directly to designated points without concerning the path taken. This method is suitable for operations that do not require precise path accuracy but need rapid movement between points.
Line Management: Ensures the tool moves in a straight line from one point to another, adhering strictly to linear trajectories parallel to the machine’s guides. Common in lathes and milling machines, this method is somewhat limited in handling complex paths.
Contour Management: The most advanced control type, allowing for intricate movements along predefined contours. This method is critical for machines designed to handle complex spatial and planar profiles, such as advanced lathes, milling machines, and grinders.

## Slide 6: Types of Numerical Control in NUMA Systems
Operational Characteristics:
Technological Operations: Each control type is tailored to the machine's capability and the complexity of the task, from simple point-to-point movements to complex contour following, enhancing both efficiency and precision.
Interpolation Techniques: Essential for contour management, where the tool path is divided into small, manageable segments for precision. Two primary forms of interpolation are:
  Linear Interpolation: Direct movement between two points, either in 2D or 3D space, useful for straightforward profiles.
  Circular Interpolation: More complex, used for creating rounded profiles where the machine calculates the necessary arc segments based on specified radii and center points.

## Slide 7: Types of Numerical Control in NUMA Systems
Technical Implications:
Memory and Programming Demand: Advanced interpolation, especially circular, requires significant computational resources and memory capacity to manage the detailed coordinates and adjustments during machining.
Precision in Execution: The level of control and interpolation directly influences the quality and accuracy of the final product, with higher control complexity leading to finer detail and higher precision in manufactured parts.
Conclusion:
The choice of numerical control type significantly impacts the machine's operational flexibility, precision, and efficiency. Advanced systems that incorporate contour management with sophisticated interpolation capabilities are leading the way in modern manufacturing, enabling the production of highly detailed and complex parts.