## Slide 1: CONTEMPORARY PRODUCTION TECHNOLOGIES
Prof. dr. Stojanche Nusev

## Slide 2: PROGRAMMING OF NU MACHINES
Types of Programming:
Manual Programming: Involves extensive calculations by the programmer to directly input commands into the machine via a suitable interface like a keyboard.
Computer-Assisted Programming: Utilizes specialized software and programming languages designed to simplify complex tasks such as trajectory calculations, significantly easing the programming process.
Programming Media:
Programs can be stored on various media such as punched tape, magnetic tape, or magnetic diskettes, or entered directly into the machine's memory.
Programming Languages:
A variety of programming languages are developed specifically for NU machine programming, including ART (Automatically Programmed Tools), which serves as the foundation for many contemporary languages like ADA PT, IFAPT, MINIAPT, etc.

## Slide 3: PROGRAMMING OF NU MACHINES
Direct Numerical Control (DNC):
DNC systems allow for direct communication between the digital counter and the control unit, facilitating real-time programming and adjustments.
Program Content and Structure:
Command Structure: Program lines are prefixed with an 'N' followed by a number indicating the sequence. Each line includes:
  G-Function: Specifies the type of operation.
  X, Y Coordinates: Defines movement along the axes.
  F-Function: Indicates the feed rate.
  S-Function: Sets the spindle speed.
  T-Function: Identifies the tool used.
  M-Function: Represents miscellaneous functions.
Example: N18 G01 X028000 Z014000 F300 S110 T102 M04 details a specific operation within the program.
Fig. 1.11. Automatic processing cycles :
po the axis x(G38)h b) po axis z (G37); c) thread cutting (G34)

## Slide 4: PROGRAMMING OF NU MACHINES
Advanced Control Functions:
G-Functions control basic operations like positioning, interpolation, and thread cutting, while M-Functions manage machine-specific tasks such as tool changes and coolant flow.
Practical Application Example:
Demonstrates a typical programming scenario on a NU lathe, outlining the step-by-step process of defining tool paths, setting operational parameters, and executing the machining process, culminating in precise component fabrication.