## Slide 1: CONTEMPORARY PRODUCTION TECHNOLOGIES
Prof. dr. Stojanche Nusev

## Slide 2: Treatment with Ultrasound
Introduction to Ultrasonic Treatment
Purpose and Scope: Discusses the utilization of ultrasonic oscillations in industrial processes, either as a standalone method or to enhance other conventional techniques.
Mechanics of Sound: Introduction to how sound, specifically ultrasound, is used in machining through periodic oscillations of media (solid, liquid, gas).

## Slide 3: Treatment with Ultrasound
Fundamentals of Ultrasonic Waves:
Nature of Waves: Ultrasound involves elastic waves with harmonic motion characterized by amplitude (A) and wavelength (λ).
Propagation: In solids, ultrasound propagates as longitudinal waves predominantly, due to their direct alignment with wave propagation, which contrasts with transverse waves that are slower and less relevant for processing.

## Slide 4: Treatment with Ultrasound
Mathematical Description of Ultrasound:
Wave Equation: The relationship between wavelength (λ), speed of sound (c), and frequency (f) is given by λ=cfλ=fc​.
Velocity in Solids: The velocity of sound in a solid is derived from its modulus of elasticity (E) and density (ρ), where v=Eρv=ρE​​. For steel, with E=210,000×103N/m2E=210,000×103N/m2 and ρ=8400kg/m3ρ=8400kg/m3, the speed of sound is calculated.
Ultrasonic Processing Equipment:
Consists of several components including a generator for ultrasonic oscillations, an amplifier, and a converter.
Power Specifications: Generators operate within a range from 0.1 to 20 kW and frequencies from 15 to 25 kHz, capable of wide adjustments to match processing requirements.

## Slide 5: Treatment with Ultrasound
Converter Technologies:
Types: Utilizes magnetostrictive or piezoelectric converters to transform electrical energy into mechanical oscillations.
Magnetostriction: Ferromagnetic materials like nickel, iron, and cobalt alloys change dimensions under magnetic fields, facilitating ultrasonic oscillation.
Oscillation System Components:
Concentrators: Play a crucial role in amplifying oscillations from the converter to the tool, potentially increasing amplitude from about 10 μm to 25-30 μm.
Design Variations: Concentrators can be graded, exponential, or conical, each affecting the amplitude amplification efficacy.

## Slide 6: Treatment with Ultrasound
Tooling and Operational Dynamics:
Tools: Designed for specific applications such as through or blind holes, with shapes influencing oscillatory system dynamics.
Material Selection: Tools are typically made from hard metals like brass or carbon steel, chosen for their durability and impact resistance.
Applications and Limitations:
Advantages: Especially beneficial for delicate materials where traditional machining could cause damage, allowing operations like milling, drilling, and engraving.
Disadvantages: Limited by small processing areas, higher energy consumption, and significant tool wear, necessitating further advancements in technology.

## Slide 7: Treatment with Ultrasound
Tooling and Operational Dynamics:
Tools: Designed for specific applications such as through or blind holes, with shapes influencing oscillatory system dynamics.
Material Selection: Tools are typically made from hard metals like brass or carbon steel, chosen for their durability and impact resistance.
Applications and Limitations:
Advantages: Especially beneficial for delicate materials where traditional machining could cause damage, allowing operations like milling, drilling, and engraving.
Disadvantages: Limited by small processing areas, higher energy consumption, and significant tool wear, necessitating further advancements in technology.

## Slide 8: Treatment with Ultrasound
Conclusion
Versatile Processing Technique: Ultrasound utilizes high-frequency sound waves, offering a non-invasive and precise machining method, particularly effective for materials sensitive to thermal and mechanical stresses.
Advanced Equipment Setup: The ultrasonic processing setup includes sophisticated components like ultrasonic oscillation generators, amplifiers, and specialized converters (magnetostrictive or piezoelectric), tailored to meet diverse industrial needs.
Enhanced Accuracy and Efficiency: Through the use of concentrators, ultrasonic processing significantly amplifies the mechanical oscillations, enabling fine and precise machining of complex parts with minimal material wastage.
Wide Range of Applications: Ideal for delicate operations such as drilling, milling, and engraving on fragile materials like glass and ceramics, proving essential in industries requiring high precision.
Need for Development: Despite its advantages, the technique faces challenges such as limited processing area, high energy consumption, and rapid tool wear, indicating a need for ongoing technological advancements to broaden its industrial applicability.